## Slide 1: Green Mountain Power Climate Action Planning Framework
Notes: PSNH
Yellow & Orange – Legacy Trucks
Thanksgiving day storm mutual aid

## Slide 2: Topics
Vermont Climate Trends
System Impacts from Weather
Customer Impacts from Weather
Climate Hardening Technologies and Priority Areas
The Role of Innovation
High level for local for area

## Slide 3: Higher Precipitation with More Intense Events
Vermont Climate Trends
More Moisture in Atmosphere
Creates More Severe Weather
Creates More Reliability Impacts

## Slide 4: Temperatures Increasing Summer Storm Severity, Winter Wet Snow/Ice
Vermont Climate Trends
Heavier, Wetter Snow/Freezing Rain
Drier, Lighter
Snow
Higher Temps Fuel Severe T-Storms
Summer
Winter

## Slide 5: More frequent Intense storms
National Trends Impacting Vermont

## Slide 6: Intense Storms More Frequent
Vermont Experience
Couture Updating this

## Slide 7: GMP Outage Map Halloween 2019
55,000 out at peak
Storm total: 114,000
2,167 “Outage Events”
Hundreds of “Hazards”
3.75 day restoration
Damage particularly in Connecticut River Valley

## Slide 8: GMP Goal
Serve customers by avoiding impacts of severe disruption and damage experienced elsewhere in country
Climate Action Plan

## Slide 9: Priority Areas
Planning Category | Highlights
T+D | Prioritized and intensified Circuit Hardening; Utilize resilient construction techniques
Substations | Accelerate floodplain analysis & relocations
Generation | Prioritize high water event management; catastrophic event emergency operating protocols, in addition to planned upgrades
IT/OT/Telecomm | Ensure cloud-based redundancy of critical systems; establish power and telecomm redundancy for critical systems
Stakeholder Communications | Improve ability to generate targeted communications (customer and non-customer) via text, email, and robo-calls during events
Resiliency Zones | Plan with state and communities to support critical areas of Vermont for grid islanding during widespread, extended disaster events
Innovation | Continue expansion of storage to customers for safety and reliability through GMP & BYOD programs
Climate Action Plan

## Slide 10: Prioritized Communities/ MOST DIFFICULT Reliability Circuits
Lowest Reliability Ran | Circuit | Communities Served | Customer on Circuit
1 | Sharon (SH-G35) | Sharon, Strafford | 1,331
2 | East Barnard (EB-Y38) | Pomfret, Barnard | 233
3 | Londonderry (LO-G26 | Windham, Londonderry | 962
4 | East Jamaica (EJ-G7) | Townshend, Jamaica | 2,607
5 | Mount Holly (MH-G13) | Mount Holly, Shrewsbury | 1,791
6 | Rochester (RO-G62) | Rochester | 1,307
7 | Rawsonville (RA-G23) | S. Londonderry | 583
8 | Sherburne (SB-G91) | Plymouth, Killington | 1,174
9 | Pleasant Street (PS-G43) | Randolph, Braintree | 1,982
10 | Woodstock (WK-G81) | Barnard | 1,263
11 | Londonderry (LO-G27) | Londonderry, Weston | 1,844
12 | Cavendish (CV-G65) | Cavendish | 313
13 | Silver Lake (SL-W1) | Leicester, Salisbury | 292
14 | Stockbridge (ST-G45) | Stockbridge, Pittsfield | 1,026
15 | Hewitt Road (HR-G38) | Bristol, Lincoln | 2,495
16 | Randolph Center (RC-G51) | Randolph, Brookfield | 861
17 | Carvers Falls Sub (CF-G16) | Benson | 708
18 | Woodstock (WK-G82) | Woodstock | 1,008
19 | Rawsonville (GA-G22) | Jamaica, Winhall | 931
20 | Wallingford (WF-G23) | Danby, Wallingford | 2,343
Climate Hardening T&D
* Five Year Annual Ranking Average (2014-18)
Red areas are reliability challenged areas we’re going after!! We’re already concentrating on these areas, but want to move faster.

## Slide 11: Western Windham and Eastern Bennington Specific
Climate Hardening T&D
* Five Year Annual Ranking Average (2014-18)
  Rebuild of main lines that have historically had reliability issues
  After main lines are rebuilt, move out to smaller tap lines
  Already designing rebuilds of the toughest reliability areas in, Dover, Halifax, Marlboro, Readsboro, Stamford, Whitingham.
  Purchased the Jacksonville Hendrix feed to re-feed portions of Whitingham and Halifax. Rebuilt and took ownership of old National Grid line this past summer that feeds Readsboro.
  Many other rural feeds in Dover, Marlboro, Readsboro already done!!

## Slide 12
Covered Wire
  Spacer Cable Construction and Insulated Tree Wire
  Much more resilient to tree contacts
Cable in Conduit Undergrounding
  Cost-Effective, Single-Phase Distribution Undergrounding
  Drastically reduces all weather related outages
Climate Hardening T&D

## Slide 13: Substations and T&D Assets 100 Year Flood Impact Models
Climate Hardening

## Slide 14: Substation/infrastructure relocation
Rebuild priority flood area substations and related infrastructure to aid community resiliency and lessen damage
Dover Sub in located in a flood plain, would be one of the subs we would work to relocate. Only other sub in this immediate with a flood threat is Vernon.
Climate Hardening

## Slide 15: IT/Telecom/Outreach
Goal: Further improve GMP’s communications systems and related IT for disaster response and outage management.
Increase targeted customer and stakeholder outreach capability – seamless, real time, and segmented.
Improve resilience of critical GMP IT infrastructure through Cloud.
Climate Hardening IT
KC Words
Insert pic of Jocelyn

## Slide 16: Fault Detection, Locating & Isolation
Automated Fault detection, locating and isolation.
Reduces extended outages to only those customers nearest the fault.
Climate Hardening IT - Self-Healing Automation
The Automatic Switch on the Grid:
Viper Re-Closer Protection/
Detection Device

## Slide 17: How It Works
Allows critical facilities to switch to alternative feeds when outage occurs.
Self-Healing Automation

## Slide 18: Increasing storage for customers
More than 1,100 customers got backup power during Halloween Storm from Powerwalls (GMP pilots incl. BYOD)
  Batteries provided 10,500 hours of backup
  Average backup was nine hours, longest was 82 hours
  With storms increasing, more outages will occur even with hardening
Climate Resiliency

## Slide 19: Questions, feedback??
GMP will be presenting our plan to our regulators in early January
Will be doing outreach between now and then as we continue to build the plan
Climate Resiliency